## Slide 1
Theo Fens
Delft University of Technology
IDIC/EDI online seminar hydrogen, September 2020
End use of hydrogen, mobility, industry, built environment

## Slide 2: The versatility of hydrogen in end use, sector coupling
Source: hydrogen Europe April 2020 https://www.hydrogeneurope.eu/news/2x40gw-green-hydrogen-initiative-paper
2
Green power provides green hydrogen
Green hydrogen storage utilising natural gas storage infrastructure
Transporting green hydrogen storage utilising natural gas network infrastructure
Hydrogen couples the sectors mobility, industry, built environment and power.
In power hydrogen can mitigate the intermittency of solar and wind: surplus electricity is converted to hydrogen with an electrolyser and stored. When required the stored hydrogen is reconverted to electricity and heat….system integration.

## Slide 3: Future mobility will be electric, battery versus hydrogen
Tesla Model S
100 kWh battery ~600 kg
Range 475 km
120 kW fast charger, 33 min. 80% fill
Fuel Cell, Hydrogen tanks, battery ~200 kg
5 kg hydrogen; range 500 km
Fuelling station <5 min. 100% fill
Toyota Mirai
Source: TUD Ad van Wijk, 2017 http://profadvanwijk.com/
3
Video Toyota Mirai https://www.youtube.com/watch?v=LSxPkyZOU7E
Video Toyota Mirai https://www.youtube.com/watch?v=LSxPkyZOU7E

## Slide 4: Mobility: battery or fuel cell? Or both?
Specific energy H2 = 33 kWh/kg Li-Ion battery = 0.1-0.25 kWh/kg
Source: Hydrogen Europe 2020 https://hydrogeneurope.eu/zero-emission-mobility
4

## Slide 5: Cost competitiveness trajectories of hydrogen applications
Source: Hydrogen Council, Path-to-Hydrogen-Competitiveness _Full-Study-1 2019 https://hydrogencouncil.com/en/path-to-hydrogen-competitiveness-a-cost-perspective/
5
2035

## Slide 6: Hydrogen tanking stations, cooling before refuelling your car
Joule-Thomson effect
  Pressure reduction natural gas: -0.5 ˚C/bar
  Pressure reduction hydrogen: +0.035 ˚C/bar
Hydrogen pressure reduction from 80 to 15 bar: +2 ˚C
Source: Hydrogen Europe 2020 https://hydrogeneurope.eu/refueling-stations
6

## Slide 7: Evolution of hydrogen cost for mobility fueling stations, $/kg
Source: Hydrogen Council, Path-to-Hydrogen-Competitiveness _Full-Study-1 2019
https://hydrogencouncil.com/en/path-to-hydrogen-competitiveness-a-cost-perspective/
Compression for gaseous trucking, liquefaction for liquid trucking or storage for pipelines.
Gaseous trucking, liquid trucking or pipelines.
Assumes average blue and green production cost in Europe (Germany offshore wind).
7

## Slide 8: TCO ratio between FCEV/BEV vehicles
Source: Hydrogen Council, Path-to-Hydrogen-Competitiveness _Full-Study-1 2019
https://hydrogencouncil.com/en/path-to-hydrogen-competitiveness-a-cost-perspective/
No. average of 5 car segments ranging from small and low usage to large and high usage.
8

## Slide 9: Cost competitiveness trajectories of hydrogen applications
Source: Hydrogen Council, Path-to-Hydrogen-Competitiveness _Full-Study-1 2019 https://hydrogencouncil.com/en/path-to-hydrogen-competitiveness-a-cost-perspective/
9
2035

## Slide 10: Stad aan ‘t Haringvliet, Het Innovathuis
Source: https://wonenopflakkee.nl/initiatieven/het-innovathuis/ , 2019
All required permits granted by June 2020.
10
New district of 100 houses planned for 2021.

## Slide 11: Testing 3 domestic boilers on hydrogen with a power-to-gas project
Source: Stedin 2019 https://tvvlconnect.nl/thema/waterstof/blog/91-waterstofverwarming-van-demonstratie-naar-echt
11

## Slide 12: Hydrogen infrastructure EU corridor split up in 15 interconnected sections
Source: TUD Jeroen Eble, March 2020 https://repository.tudelft.nl/islandora/object/uuid%3A8b0c8cf7-ac12-4ba1-a604-04dd9f85b39d
The EU Blue Banana corridor is eligible for kick starting the hydrogen economy.
Current industrial hydrogen use
Existing natural gas infrastructure
Salt cavern storage
Population density for hydrogen use in domestics and mobility
12

## Slide 13: Potential hydrogen storage capacity in salt caverns in Europe
Source: Ad van Wijk, TUD, 2019
< 50 km to shore
Storage capacity: onshore 23,200 TWh, offshore 68,800 TWh
13

## Slide 14: Thank you for your attention
14

## Slide 15: Backup sheets
15

## Slide 16: Fuel cell cars versus battery electric vehicle
Source: Energy Post 2020
https://energypost.eu/energy-conversion-for-hydrogen-cars-is-only-half-that-for-bevs/
In case of the fuel cell electric vehicle the overall efficiency in the power-to-vehicle-drive energy chain is roughly half the level of a battery electric vehicle.
Status end 2019:
BEV: 5,000,000
FCV: 7,500
16

## Slide 17: Fuel cell based micro CHP
Source: Albert van den Noort DNVGL 2018
17

## Slide 18: Hydrogen tanking stations NL
Source: Opwegmetwaterstof 2020 https://opwegmetwaterstof.nl/tanklocaties/
18

## Slide 19: Cost competitiveness trajectories of hydrogen applications
Source: Hydrogen Council, Path-to-Hydrogen-Competitiveness _Full-Study-1 2019 https://hydrogencouncil.com/en/path-to-hydrogen-competitiveness-a-cost-perspective/
19

## Slide 20: Economics of synfuel production 2030 for aviation and shipping
Source: IIRENA nov 2019
20

## Slide 21: Green hydrogen production costs development 2020-2050
Source: TUD van As & Hellinga, 2019
21