## Slide 1
Theo Fens
Delft University of Technology
IDIC/EDI online seminar hydrogen, September 2020
Long-term potential of hydrogen, expected developments

## Slide 2: Green hydrogen, the financials of PEM technology
 | Investment cost [€/kW] | Efficiency | Electricity Price Offshore Wind [€/MWh] | Hydrogen Price [€/kg]
Till 2020 | 600-900 | 72-75% | 40-50 | 3-4
2020-2025 | 300-600 | 75-78% | 30-40 | 2-3
2025-2030 | 250-400 | 78-80% | 25-35 | 1.5-2.5
After 2030 | <250 | >80% | 20-30 | 1-1.5
Source: TUD Ad van Wijk, 2019 http://profadvanwijk.com/
2
In 2025-2030 price parity green hydrogen with grey/blue hydrogen.

## Slide 3: Learning rates for hydrogen generation and applications
Source: Hydrogen Council, Path-to-Hydrogen-Competitiveness _Full-Study-1 2019 https://hydrogencouncil.com/en/path-to-hydrogen-competitiveness-a-cost-perspective/
Installed base: assuming 50/50 split of electrolysers volume with 50-75% utilisation; assuming 115 kW for PV, 250 kW for buses and 300 kW for trucks; LCOE used for solar cost; batteries in MWh.
3
Capex development of selected technologies over total cumulative production, indexed to 2020 values (2010 for comparative technologies).

## Slide 4: Green hydrogen production costs development 2020-2050
Source: TUD van As & Hellinga, 2019
4

## Slide 5: Power to X concept, integrated utility, electricity, heat and water
Source: Solar power to the people,2018 http://profadvanwijk.com/books/solar-power-to-the-people/
Usage
Source
Conversion & storage
5

## Slide 6: Power to X concept, system integration, major role for storage
Source: Solar power to the people,2018 http://profadvanwijk.com/books/solar-power-to-the-people/
Home batteries in houses
6

## Slide 7: An integrated, multi energy grid in the Netherlands? Combined TSO study
Source: Gasunie Tennet 2020 https://www.tennet.eu/fileadmin/user_upload/Company/News/Dutch/2019/Infrastructure_Outlook_2050_appendices_190214.pdf
7

## Slide 8: EU hydrogen strategy published July 2020
Source: EU Hydrogen Strategy EC July 2020 https://ec.europa.eu/commission/presscorner/detail/en/FS_20_1296
What does the roadmap for this formidable challenge look like?
8

## Slide 9: The path towards a European hydrogen eco-system step by step
9
Source: European Commission 2020
https://ec.europa.eu/energy/topics/energy-system-integration/hydrogen_en
How about the green power for all this green hydrogen?

## Slide 10: Solar irradiation and wind speed in Europe and North Africa
Source: TUD Ad van Wijk, 2017 http://profadvanwijk.com/
10

## Slide 11: Symbiotic hydrogen project North-Africa and Europe
Source: A North Africa - Europe Hydrogen Manifesto, van Wijk et al,, 2019
https://dii-desertenergy.org/wp-content/uploads/2019/12/Dii-hydrogen-study-November-2019.pdf
Energy Balance European Union 2050; primary energy production is 15,710 TWh, with
final energy consumption amounting to 12,000 TWh.
11

## Slide 12: First moving carbon beds for methane pyrolysis: combined reaction and heat integration
Source: BASF SE November 2019 https://www.efzn.de/fileadmin/documents/Niedersaechsische_Energietage/Vortr%C3%A4ge/2019/NET2019_FF1_04_Bode_Rev1.pdf
12

## Slide 13: Green hydrogen: water electrolysis or methane pyrolysis?
Source: BASF SE November 2019 https://www.efzn.de/fileadmin/documents/Niedersaechsische_Energietage/Vortr%C3%A4ge/2019/NET2019_FF1_04_Bode_Rev1.pdf
13

## Slide 14: Cost competitiveness of methane pyrolysis
Source: BASF SE November 2019 https://www.efzn.de/fileadmin/documents/Niedersaechsische_Energietage/Vortr%C3%A4ge/2019/NET2019_FF1_04_Bode_Rev1.pdf
14

## Slide 15: Hydrogen directly from solar panels
Source: KU Leuven 2019 https://nieuws.kuleuven.be/en/content/2019/belgian-scientists-crack-the-code-for-affordable-eco-friendly-hydrogen-gas
Bioscience engineers from KU Leuven have designed a hydrogen panel that converts 15 per cent of the sunlight straight into hydrogen gas – a world record.
15

## Slide 16: Hydrogen directly from solar panels using water splitting
Source: Australian National University 2020 https://onlinelibrary.wiley.com/doi/epdf/10.1002/aenm.202000772
Australian researchers have claimed a new world efficiency record of 17.6% for solar panels that can directly split water using sunlight. They use a photoelectrochemical (PEC) solar-to-hydrogen (STH).
The low-cost layered perovskite is combined with a convectional Si solar cell should lead to low cost hydrogen.
16

## Slide 17: Thank you for your attention
17

## Slide 18: Backup sheets
18

## Slide 19: Northern part Netherlands, a hydrogen hub
Source: New Energy Coalition 2019
Transition from a natural gas hub towards a hydrogen hub. Utilisation of the current infrastructure including salt cavern storage.
19

## Slide 20: Northern part Netherlands, a stepwise development plan
Source: New Energy Coalition 2019
By linking individual projects and developing local H2 infrastructure, establishing H2 Valleys represents the next development stage towards a local H2 economy in the long term
H2 Valleys should establish local H 2 nuclei or from which further roll out and uptake of local H2 use can be started
Implementing H2 Valleys should be part of a clear local strategy to start a long-term green energy transition and be backed up by respective political commitment
20